## Slide 1
IEEE Conference Presentation
Selective Kernel Domain Adaptation
with LMMD Alignment for
Milling Machine Fault Diagnosis
Saif Ullah | Muhammad Umar | Jong-Myon Kim
Department of Electrical, Electronic and Computer Engineering | University of Ulsan, South Korea
Fault Diagnosis
Domain Adaptation
Transfer Learning
Condition Monitoring
Funded by MOTIE Korea • Technology Innovation Program (20023566)

## Slide 2
THE PROBLEM
57%
of mechanical breakdowns
caused by tool wear,
bearing & gear defects
⚠ Distribution Shift
Vibration signals at different spindle speeds follow different statistical distributions
📉 Model Degradation
Deep learning models trained at one speed fail when applied to another operating condition
🔍 No Target Labels
In real scenarios, labeled data for new operating conditions is unavailable
2

## Slide 3
PROPOSED SOLUTION
SK-DA Network + LMMD Alignment
1D Conv
SK-CNN
Raw vibration → multi-scale feature extraction with adaptive receptive fields
LMMD
Alignment
Class-aware distribution matching between source & target speeds
Joint
Training
Labeled source + unlabeled target trained simultaneously
3

## Slide 4
EXPERIMENTAL SETUP
Machine & Acquisition
Machine
INTER SIEG X1 Micro Mill Drill
Sensors
Accelerometers (spindle + motor)
DAQ
NI 9234 @ 25,600 Hz
Spindle Speeds
1320 rpm & 1440 rpm
Feed Rate
0.4 mm/s (constant)
Fault Types
Normal · Tool · Bearing · Gear
Dataset Samples
Speed | Normal | Gear | Tool | Bearing
1320 rpm | 116 | 111 | 112 | 112
1440 rpm | 112 | 110 | 112 | 112
NORMAL
TOOL FAULT
BEARING FAULT
GEAR FAULT
Faults induced per ISO 8688-2: 0.3mm flank wear, 3mm bearing cut, removed gear tooth section
4

## Slide 5
METHODOLOGY: SIGNAL PROCESSING PIPELINE
Raw Vibration
Signal
25,600 Hz sampling
Signal
Segmentation
Overlapping windows
preserve fault impulses
SK-CNN
Feature Extraction
1D Conv + Selective
Kernel Attention
LMMD Domain
Alignment
Class-wise distribution
matching
Fault
Classification
Softmax over 4
fault categories
SOURCE DOMAIN
1320 rpm — Labeled
(4 fault classes)
Classification Loss (Cross-Entropy)
guides fault identification
TARGET DOMAIN
1440 rpm — Unlabeled
(no annotations needed)
LMMD Alignment Loss
enforces speed-invariant features
↔
5

## Slide 6
SELECTIVE KERNEL FEATURE EXTRACTOR
Input
Signal X
Conv k₁ BN ReLU → F₁
Conv k₂ BN ReLU → F₂
+
GAP
→ z
Softmax
α₁, α₂
Y = α₁F₁
+ α₂F₂
KEY INSIGHT
Unlike fixed-kernel CNNs, the SK block dynamically selects the optimal temporal receptive field for each fault type — tool wear requires different signal patterns than bearing defects.
Multi-scale
Capture
Two parallel convolution branches with different kernel sizes k₁, k₂ capture both local and global fault patterns
Adaptive
Weighting
Attention weights α₁, α₂ from Softmax allow the network to emphasize the most relevant receptive field
End-to-End
Learning
No handcrafted features — the network learns discriminative representations directly from raw vibration samples
6

## Slide 7
LMMD DOMAIN ALIGNMENT
Conventional MMD
✗ Aligns overall (marginal) distributions
✗ Ignores class structure during alignment
✗ May mix features from different fault types
✗ Less discriminative for fine-grained faults
Label-aware LMMD ✦
✓ Aligns class-conditional distributions
✓ Matches each fault class separately across speeds
✓ Preserves inter-class separability
✓ Achieves speed-invariant discriminative features
VS
Total Loss: L_total = L_cls + λ × L_lmmd
7

## Slide 8
RESULTS: CASE 1 — 1320 rpm → 1440 rpm
Source: 1320 rpm (Labeled)
→ Knowledge Transfer →
Target: 1440 rpm (Unlabeled)
Confusion Matrix
100%
Accuracy
All 4 fault classes correctly identified with ZERO misclassifications across all target domain samples
ROC Curves
AUC = 1.0
All Classes
Perfect separation between healthy and faulty conditions across all classes in the unseen target speed
t-SNE Visualization
4 Distinct
Clusters
4 clearly separated compact clusters — no overlap between fault categories confirming LMMD alignment success
8

## Slide 9
RESULTS: CASE 2 — 1440 rpm → 1320 rpm
Reversed Direction: Source 1440 rpm → Target 1320 rpm | Validates bidirectional transfer capability
100%
Classification Accuracy
All samples correctly classified
1.0
AUC Score
Perfect ROC for all 4 fault classes
4/4
Feature Clusters
Well-separated t-SNE clusters
0
Misclassifications
Zero errors across all conditions
The model generalizes in BOTH transfer directions — confirming speed-invariant feature learning
9

## Slide 10
KEY CONTRIBUTIONS
01
Cross-Speed Diagnostic Framework
Domain adaptation enabling knowledge transfer between different spindle speeds without target labels
02
1D Selective Kernel CNN
Multi-scale fault pattern learning directly from raw vibration — no time-frequency image conversion needed
03
Class-aware LMMD Alignment
Reduces feature distribution mismatch at the class level, preserving discriminability across operating speeds
04
Practical Industrial Solution
Validated on real milling machine data — deployable for tool condition monitoring in manufacturing
10

## Slide 11
CONCLUSION
A Selective Kernel Domain Adaptation Network with LMMD alignment successfully overcomes the cross-speed distribution shift challenge in milling machine fault diagnosis — achieving perfect classification in both transfer directions without any target domain labels.
⚙
No Time-Frequency
Conversion Needed
🎯
Speed-Invariant
Fault Features
🏭
Practical Predictive
Maintenance Ready
Future Work: Extend to multi-speed scenarios, other rotating machinery, and online adaptive learning
Thank you for your attention! | saifuou@mail.ulsan.ac.kr | University of Ulsan, South Korea
11